Sigma 33 East Coast Association

49 Bellevue Road,

Glenageary,

Co.Dublin.

Hon Sec Sandra Moore

087 629 1568

# SIGMA 33 OOD Standard Inspection Form 2008

Important  Inspection is carried out only as a guide to owners.  You are only compliant if you have a “YES” answer for all questions.  An inspector cannot limit or reduce the complete and unlimited responsibility of the owner or owner’s representative.

Yacht Name 								  Sail No. 	_______

“I, owner or representative, have read and understand the Sigma 33 Class Rules and ORC Special Regulations, in particular 1.01, 1.02, 2.02 and 2.03.”

It should be noted that all members acting as helmsman or entering a Sigma 33 in races which consist of, or include the Class, shall be members of the Sigma 33 OOD Class Association.

Signed 								Printed		 	___________

Please prepare your yacht as requested.  This will save everybody time!  Have somebody ready on the boat who is thoroughly familiar with her gear (as all crew members must be).  Failure to comply may result in a penalty or exclusion from a race or race results.  The inspector may check items not listed here.

Please lay out items marked* on a clear berth.  Thank you for your help.

## CLASS RULES

*	  1.	Is the current IRC/RORC or a Sigma Assn One-Design Certificate on board and signed?	Yes/No

2.	Is the hull coated with antifouling paint, and kept in good repair?	Yes/No

## Spars and Rigging

3.	No alterations may be made to extrusions to lighten them – do you comply?	Yes/No

4.	One spinnaker halyard (made of synthetic rope).  This may exit from the port side of mast.	Yes/No

5.	Do the Main and Genoa halyards exit from mast heel casting?	Yes/No

6.	Is the Forestay luff foil less than 32mm fore and aft? Is it on a 7mm wire forestay?	Yes/No

7.	Hydraulic, electric or pneumatic actuators are prohibited – do you comply?	Yes/No

8.	Is there only one spinnaker pole of approved type – stowed as in rule 10.4?	Yes/No

- Is all standing rigging made from 1 x 19 wire?  Individual strands to be of round section,

Or alternatively Dyform material of the same dimensions may be used. 	Yes/No

10.	Running backstays are not permitted – do you comply?	Yes/No

11.	Does the backstay system comply with rule 8.12?	Yes/No

## Sails

12.	Are the Main, No 1, No 2, Working Jib, Storm Jib, light and heavy spinnakers, all on board?	Yes/No

- No additional sails are permitted on board except for storm trysail or old fore and aft sails

As provided in rule 11.2 – do you comply?	Yes/No

Deck Gear

- 7 Winches –  on the Mast, 2 coachroof, 2 primary cockpit, 2 secondary cockpit – none more

than two speed.  Power ratio’s not exceeding original specification – do you comply?	Yes/No

15.	Is there only one genoa sheet track on each side deck?	Yes/No

16.	Are the Cockpit gratings in place, and the Bridge deck on board?	Yes/No

- Are there two anchors and two fathoms of 5/16” (8mm) chain stowed and secured with lashings

Forward of the forward bulkhead?  Minimum weight 15lbs (6.80kg) and 25lbs (34kg)?	Yes/No

18.	Is a Gas bottle, minimum 12lbs (5.44kg), stowed in its locker?	Yes/No

19.	Does the Fuel tank have a minimum capacity of 68 litres (approx 15 gallons)?	Yes/No

Below Deck

20.	Is all interior joinery as originally fitted with no lightening holes (which are prohibited)?	Yes/No

21.	Are all linings in place, and the table in its normal position?	Yes/No

22.	Is the cooker as originally fitted, or one of equivalent weight, in place?	Yes/No

- Are all berth cushions in their normal position (except half berth)?  Half berth cushion

must be on board.  (Except as provided in rule 13.3).	Yes/No

24.	Is the toilet as originally supplied, or one of equivalent weight, in place?	Yes/No

25.	Are there two batteries, of minimum weight 29kg each, stowed in place?	Yes/No

26.	Are there two watertanks, of minimum capacity 180 litres, under saloon berths?	Yes/No

27.	Is there a minimum of 20 litres of fuel in the permanent installed tank?	Yes/No

28.	Is there a Marine radio transceiver with masthead antenna, and emergency antenna?	Yes/No

ORC CATEGORY 4 SPECIAL REGULATIONS (ORC regulation number in brackets)

29.	Is all equipment securely fastened (tool box, batteries, cooker etc.)  (2.03.02 b)	Yes/No

- Are the washboards/companionway hatch capable of being fastened and unfastened from above

and below deck and capable of being secured so that they cannot be lost overboard?  (3.08.04)	Yes/No

31.	Are there double Lifelines all round the boat (including pulpit and pushpit)?  (3.14.03)	Yes/No

- Are the Lifelines taut?  As a guide, when deflecting force of 50N (5.1 kgf./11.2 lbf) is applied to

a lifeline midway between supports, the lifeline should not deflect more than 50mm.  (3.14.2)	Yes/No

33.	Bilge pumps must not be connected to cockpit drains – do you comply? (3.23.2)	Yes/No

- Is there one manual Bilge Pump, and is its handle attached to the boat with a lanyard to

prevent loss?  (3.23.4)	Yes/No

*	35.	Are there 2 STOUT buckets with lanyards? (minimum capacity 9 litres)  (3.23.5.f)	Yes/No

36.	Is a marine type Compass properly installed and adjusted?  (3.24.1.a)	Yes/No

*	37.	Are there Navigation Lights (3.27) with spare bulbs – Minimum power 10 watts?  (3.27.5)	Yes/No

*	38.	Is there a Flashlight?  Is it water resistant with spare bulbs and batteries?  (4.07.1.b)	Yes/No

39.	Is there a Radio receiver capable of receiving weather bulletins?  (3.29.1.ciii)	Yes/No

40.	Are there softwood plugs of appropriate size adjacent to all seacocks (attached)?  (4.03)	Yes/No

41.	Are there 2 fire extinguishers easily accessible located in different area of the boat?  (4.05)	Yes/No

*42.	Is there a First Aid Kit with manual, foghorn and radar reflector?  (4.08, 4.09, 4.10)	Yes/No

43.	Are there Charts (not solely electronic), light lists and piloting equipment? (4.11)	Yes/No

- Is a durable stowage chart provided, displayed where it can be best seen in the main ,

Accommodation, marked with items of safety equipment.  (4.12)	Yes/No

45.	Is there an echo or lead line sounder?  (4.13)	Yes/No

*	46.	Are there Tools and Spare Parts, including a means of quickly severing standing rigging?  (4.16)	Yes/No

47.	Is the Yacht’s name on miscellaneous buoyant equipment?  (4.17)	Yes/No

48.	Is there Marine grade reto-relective material on lifebuoy, lifeslings and lifejackets etc?  (4.18)	Yes/No

*	49.	Is there a Lifebuoy with a self-igniting light and a drogue, or a Lifesling with a self-igniting

light and without a drogue, near to the helmsman?  (4.22.1.a)	Yes/No

*	50.	Are there 4 red and 4 white hand flares, 2 orange floating smoke signals?  (not hand held)  Do

they confirm to SOLAS Regulations?  Are they not older than the stamped expiry date, or if no

expiry date stamped not older than 4 years old and stowed in a waterproof container(s)?  (4.23.1)	Yes/No

51.	Is there a Heaving Line, readily accessible in the cockpit, and of 15m – 25m length?  (4.24)	Yes/No

52.	IS a knife provided, which is readily accessible from the deck or cockpit.  (4.25)	Yes/No

*	53.	Is there a Lifejacket, with a whistle, fitted with marine grade retro-reflective material,

compatible with the wearer’s safe harness and if inflatable , regularly checked for air

retention and clearly marked with the yacht’s or wearer’s name for each crew member?

Note recommendations for a light, crotch strap and splashguard.  (5.01)	Yes/No

54.	Each crew member shall have a safety harness, and safety line not more than 2m long with a

snaphook at each end.

Warning it is possible for a plain snaphook to disengage from a U-bolt if the hook is rotated

under load right-angles to the axis of the U-bolt.  For this reason the use of snaphooks with positive

locking devices is strongly recommended.(5.02.1)

Passed inspection / Failed inspection.  Items to be reinspected

______________________________________________________________________________________

Inspector

Signed